 For loop:

A loop is used for executing a block of statements repeatedly until a particular condition is satisfied.

#include<iostream>
using namespace std;
int main()
{
    int arr[5] = {2, 3, 4, 5, 8};
    for(int i = 0; i<5; i++)
   {
cout<<arr[i]<<endl;
   }

return 0;
}

In for loop first we need to initialize and then check the condition and increment i value and it will be repeated until condition gets failed.

In C++11 Range Based Loops

In C++11 extends the syntax of the for statement to allow for easy iteration over a range of elements.
such as all elements in a container.
//Basic Example:

#include<iostream>
using namespace std;
int main()
{
int arr[5] = {2, 3, 4, 5, 6};
for(auto i: arr)
{
cout<<i<<endl;
}
return 0;
}
//Sample program:

#include<iostream>
#include<vector>
using namespace std;

int main()
{
vector<int> v = {2, 3, 5, 6, 7, 8, 9};

for(auto x: v)
{
cout<<x<<endl;
}
}

#include<iostream>
#include<vector>
using namespace std;
int main()
{
vector<int> v = {2, 3, 5, 6, 7, 8, 9};

for(auto &x: v) // Type reference by reference .
//Preferred when modifies is requried
{
x++;
}
for(auto x: v)
{
cout<<x<<endl;
}
}

// sample program

#include<iostream>
#include<map>
using namespace std;

int main()
{
//	map<int, string> m ({{1, "eat"}, {2, "code"}, {3, "sleep"}});
    map<int, string> m;
    m.insert({1, "eat"});
    m.insert({2, "code"});
    m.insert({3, "sleep"});

for(auto c: m)
{
cout<<c.first<<"\t"<<c.second<<endl;
}
}

for_each:

This loop executes over each of the container elements.
This loop is defined in the header file “algorithm”
for_each takes three arguments.
*First argument takes Beginning position.
*Second arguiments takes Ending position.
*Third argument takes either function name or function object or lambda function.

Basic Sample:

#include<iostream>
#include<algorithm>
using namespace std;

// for_each using function pointer

void print(int a)
{
    cout<<a<<endl;
}

int main()
{
int a[3] = {4, 5, 6};
for_each(a, a+3, print);
}

// for_each using lambda function

#include<iostream>
#include<vector>
#include<algorithm>
using namespace std;

int main()
{
vector<int> vec = {2, 3, 4, 5};
for_each(vec.begin(), vec.end(), [](int v)
{cout<<v<<endl;}
);
}

//for_each using function objects

#include<iostream>
#include<algorithm>
using namespace std;

class A
{
public:
void operator()(int v)
{
cout<<v<<endl;
}
};

int main()
{
A obj;
int a[5] = {2, 3, 4, 6, 7};
for_each(a, a+5, obj);
return 0;
}

 what is Function:

A function is a group of statements that together perform a task.
A function declaration tells compiler about a function name, return type and parameters.And function definition.

USE:
Instead of writing same code again and again for diffferent inputs. We can call the function.[We can reuse the function].

// Sample

#include<iostream>
using namespace std;
int add(int a, int b)
{
return a+b;
}
int main()
{
cout<<add(1, 2)<<endl;
cout<<add(6, 7)<<endl;
return 0;
}

what is Lambda function?

It is introduced in c++11.
It can be used for short snippet of code that are not going to reuse.
Lambda function is a anonymous functions.
It doenot have return type.
Syntax:
[capture clause](parameters)->return type
{//body}

//1 type
int main()
{
    cout<<[](int a, int b){return a+b;}(5, 2)<<endl;
}

Disadv:
we cannot reuse.

//2nd type

int main()
{
   auto f = [](int a, int b)
{return a+b;};

    cout<<f(2,5)<<endl;
    cout<<f(7, 8)<<endl;

}

//sample
auto f = [](int a, int b)
{return a+b;};

int main()
{
    cout<<f(2,5)<<endl;
    cout<<f(7,5)<<endl;
    cout<<f(5,5)<<endl;
}

For different arguments:

#include<iostream>
using namespace std;

int main()
{
   auto f = [](int a, int b)
{cout<<"a:"<<a<<"\t"<<"b:"<<b<<endl;};

    f(2,5);

    f(74.4, 84.5);
    f('a', 'b');
}

Here we can observe narrowing, double converted into int and char converted to int.

In c++14 we can avoid:

#include<iostream>
using namespace std;

int main()
{
   auto f = [](auto a, auto b)
{cout<<"a:"<<a<<"\t"<<"b:"<<b<<endl;};

    f(2,5);

    f(74.4, 84.5);
    f('a', 'b');
}

How to capture local variables inside Lambda?

Local variables from outer scope can be captured inside Lambda in 2 modes i.e.
1. by value
2. by reference

## Capturing Local Variables by value inside Lambda Function
To capture the local variables by value, specify their name in capture list.Now the variables specified in captured list is copied inside lambda by value . We can access the values.But we cannot modify it.because they are const.
#include<iostream>
using namespace std;
int main()
{
    int x = 10;
    int y = 42;
    auto q = [ x, y] ()
    {
        cout << "x: " << x<< endl; //x:10
       cout << "y: " << y <<endl; //y:42
       x = 20; //error: read_only variable x
       y = 40; //error: read_only variable y
    };
    q();
}
To Modify:
we can use mutable to modify the captured variables.But the modification will not affect the outer scope variables, because they are captured by value.
//sample
#include<iostream>
using namespace std;
int main()
{
    int x = 10;
    int y = 42;
    auto q = [ x, y]() mutable
    {
        cout << "x: " << x<< endl;
       cout << "y: " << y <<endl;
       x = 20;
       y = 40;
       cout << "x: " << x<< endl;
       cout << "y: " << y << endl;
    };
    q();
       cout << "x: " << x<< endl;
       cout << "y: " << y << endl;
}

## Capturing Local Variables by reference inside Lambda Function:
To capture the local variables by reference, specify their name in capture list and prefixed with “&”.Now the variables specified in captured list is copied inside lambda by reference . We can access the values and also we can modify it. And modification will affect the outer scope variables.
//sample
#include<iostream>
using namespace std;
int main()
{
    int x = 10;
    int y = 42;
    auto q = [ &x, &y]()
    {
        cout << "x: " << x<< endl;
       cout << "y: " << y <<endl;
       x = 20;
       y = 40;
       cout << "x: " << x<< endl;
       cout << "y: " << y << endl;
    };
    q();
       cout << "x: " << x<< endl;
       cout << "y: " << y << endl;
}
To capture all local variables from outer scope by value just use “=” in the capture list
 // auto q = [ =]() mutable {};

To capture all local variables from outer scope by reference just use “&” in the capture list
 // auto q = [ &]() mutable {};

We can mix capturing by value and reference
//auto q = [ =, &y]() mutable {};

Note: Becareful while capturing local varaibles by reference in lambda[segmentation fault]
# To capture member variables inside Lambda function
If we trying to capture member variable directly by value or reference, then it will not work. We will get compile time error.
//sample
#include<iostream>
#include<vector>
#include<algorithm>
using namespace std;
class A
{
int mcnt;
public:
A()
{
    mcnt = 0;
}
void update(vector<int> &vec)
{
//error: capture of non-variable
for_each(vec.begin(), vec.end(), [mcnt](int x)
{
        if(x%2 == 0)
        mcnt++;
    });
}
int getcount()
{
return mcnt;
}
};
int main()
{
vector<int> vec = {4, 2, 5, 6};
A obj;
obj.update(vec);
cout<<obj.getcount()<<endl;
return 0;
}
To capture the member variables inside lambda function, capture the “this” pointer by value .
Capturing this pointer inside lambda function will automatically capture all the member variables for this object inside lambda.
//sample
#include<iostream>
#include<vector>
#include<algorithm>
using namespace std;
class A
{
int mcnt;
public:
A()
{
    mcnt = 0;
}
void update(vector<int> &vec)
{
//error: capture of non-variable
for_each(vec.begin(), vec.end(), [this](int x)
{
        if(x%2 == 0)
        mcnt++;
    });
}
int getcount()
{
return mcnt;
}
};
int main()
{
vector<int> vec = {4, 2, 5, 6};
A obj;
obj.update(vec);
cout<<obj.getcount()<<endl;
return 0;
}

Function Overriding
redefining the base class function in the derived class with same signature i.e, return type and parameters.

Override
The override is a special identifier means that the compiler will check the base if their is any virtual function with this exact signature.if there is not compiler will throw error.
Override may appear immediately after the declarator
It tells the reader also that is overriding a virtual method of base class.
//sample
#include<iostream>
using namespace std;
class A
{
    public:
    virtual void f(int a)
    {
        cout<<"A::f"<<endl;
    }
   virtual void fun()
    {
        cout<<"A::f"<<endl;
    }
};
class B:public A
{
    public:
//error:virtual void B::f(double ) marked override
     virtual void f(double a) override
    {
        cout<<"B::f"<<endl;
    }

};
int main()
{
    A *p = new B;
    p->f(10);
    return 0;
}
In above program it has different signature so, it will create second virtual function.

Unordered_set
It is a STL container and it is introduced in c++11.
It is defined in the header file #include<unordered_set>
It contains only unique elements only.
Elements will be stored in any order.
Hash_table used to store elements.
We can erase the element in the container.
//sample
#include<iostream>
#include<unordered_set>
using namespace std;
int main()
{
    //inserting the elements in the container using intialization list
    unordered_set<int> m1 = {7, 8, 9, 2, 2};

    //inserting the element in the container
   /* m1.insert( 2);
    m1.insert(2);
    m1.insert(1);
    m1.insert(12);
    m1.insert(5);
    m1.insert(99);*/

    //printing the element in the container using Range based loop
    for(auto i: m1)
    {
        cout<<i<<endl;
    }
    //printing the element in the container
   /* for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<*it<<endl;
    }
     cout<<"\n"<<endl;
     */
     //finding the element wheather it is present are not
     int key = 12;
     if(m1.find(key) == m1.end())
     {
        cout << key << " not found\n";
     }
    else
    {
        cout << "Found " << key << endl;
    }
        cout<<"\n"<<endl;

     //Erasing the element
    auto it = m1.begin();
    ++it;
    m1.erase(it);
    for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<*it<<endl;
    }
    cout<<"\n"<<endl;
    cout<<m1.size()<<endl;
    cout<<m1.max_size()<<endl;
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    m1.clear();
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    return 0;
}
Unordered_multiset
It is a STL container and it is introduced in c++11.
It is defined in the header file #include<unordered_set>
Elements are stored in any order.
It will allow duplicate elements also.
We can erase the element for which iteration position is given.
//sample
#include<iostream>
#include<unordered_set>
using namespace std;
int main()
{
    //inserting the elements in the container using intialization list
   // unordered_multiset<int> m1 = {7, 8, 9, 2, 2};
    unordered_multiset<int> m1;
    //inserting the element in the container
    m1.insert( 2);
    m1.insert(2);
    m1.insert(1);
    m1.insert(12);
    m1.insert(5);
    m1.insert(99);

    //printing the element in the container using Range based loop
    for(auto i: m1)
    {
        cout<<i<<endl;
    }
    //printing the element in the container
   /* for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<*it<<endl;
    }
     cout<<"\n"<<endl;
     */
     //finding the element whether it is present are not
     int key = 12;

     if(m1.find(key) == m1.end())
     {
        cout << key << " not found\n";
     }
    else
    {
        cout << "Found " << key << endl;
    }
        cout<<"\n"<<endl;

     //Erasing the element
    auto it = m1.begin();
    ++it;
    m1.erase(it);
    for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<*it<<endl;
    }
    cout<<"\n"<<endl;

    cout<<m1.size()<<endl;
    cout<<m1.max_size()<<endl;
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    m1.clear();
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    return 0;
}

Unordered_map
It is defined in the header file unordered_map
It will store elements in the combination of key and value.
It will not store duplicate key.
Unordered_map key will be stored in any order.
//sample
#include<iostream>
#include<unordered_map>
using namespace std;

int main()
{
    unordered_map<int, int> m1;
    // inserting an element
    m1.insert( {2, 9});
    m1.insert({12,10});
    m1.insert({1,9});
    m1.insert( {2, 9});
    m1.insert({12, 7});
    m1.insert({5, 8});
    m1.insert({99,5});

    //printing the elements
    for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<it->first<<"\t"<<it->second<<endl;

    }
     cout<<"\n"<<endl;

     //finding the element wheater it is present are not
     int key = 12;
     if(m1.find(key) == m1.end())
     {
        cout << key << " not found\n";
     }
    else
    {
        cout << "Found " << key << endl;
    }
        cout<<"\n"<<endl;

     //erasing an element
    auto it = m1.begin();
    ++it;
    m1.erase(it);
    for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<it->first<<"\t"<<it->second<<endl;

    }
    cout<<"\n"<<endl;

    //No.of elements present in container
    cout<<m1.size()<<endl;

    // maximum size of container
    cout<<m1.max_size()<<endl;

    //cout<<m1.back()<<endl;
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    m1.clear();
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    cout<<m1.size()<<endl;
    return 0;
}

Unordered_multimap

It is defined in the header file unordered_map
It will store elements in the combination of key and value.
It will allow to store duplicate key.
Unordered_multimap key will be stored in any order.
//sample
#include<iostream>
#include<unordered_map>
using namespace std;

int main()
{
    unordered_multimap<int, int> m1;
    // inserting an element
    m1.insert( {2, 9});
    m1.insert({12,10});
    m1.insert({1,9});
    m1.insert( {2, 9});
    m1.insert({12, 7});
    m1.insert({5, 8});
    m1.insert({99,5});

    //printing the elements
    for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<it->first<<"\t"<<it->second<<endl;

    }
     cout<<"\n"<<endl;

     //finding the element wheater it is present are not
     int key = 12;
     if(m1.find(key) == m1.end())
     {
        cout << key << " not found\n";
     }
    else
    {
        cout << "Found " << key << endl;
    }
        cout<<"\n"<<endl;

     //erasing an element
    auto it = m1.begin();
    ++it;
    m1.erase(it);
    for(auto it = m1.begin(); it!= m1.end(); ++it)
    {
        cout<<it->first<<"\t"<<it->second<<endl;

    }
    cout<<"\n"<<endl;

    //No.of elements present in container
    cout<<m1.size()<<endl;

    // maximum size of container
    cout<<m1.max_size()<<endl;

    //cout<<m1.back()<<endl;
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    m1.clear();
    if(m1.empty())
    {
        cout<<"container is empty"<<endl;
    }
    else
    {
        cout<<"container is not empty"<<endl;
    }
    cout<<m1.size()<<endl;
    return 0;
}